## Slide 1: McCain 2070LX Controller
Overview
Presented by:
Douglas Acker
Hardware Engineering Manager
November 16, 2017
McCain, Inc.

## Slide 2: Contents
History
Hardware
Software
Standards and testing
Advantages and disadvantages

## Slide 3: History
More powerful replacement for 170 and NEMA controllers
Established open architecture
Non application specific
Version – Caltrans ATC 1C standard
The road to the 2070LX

## Slide 4: Hardware
Open architecture
  Interchangeable components
  Defined interfaces
  Compatible with existing equipment
Common operating system software: (Linux)
Hardware specification only; no application software

## Slide 5: Hardware Components
Chassis
CPU
Field I/O
Serial and modem
Power supplies
Front panels
NEMA modules

## Slide 6: Chassis
Same 2070 chassis for any configuration

## Slide 7: CPU
Based on Freescale 8360 PowerQUICC II Pro processor
16 MB NOR Flash and 256 MB NAND Flash
2 MB SRAM
256 MB DRAM
7 Serial ports
4 Ethernet ports (10/100 Base T)
2 USB

## Slide 8: Engine Board Comparison Table
 | ATC 5.2b | ATC 6.24 | Caltrans 2070-1C | Specifications
CPU | Freescale MPC8360E @ 400 MHz | Freescale MPC8360E @ 400 MHz | Freescale MPC8360E @ 400 MHz | 60MIPS
DRAM | 128 MB (256 MB optional) | 256 MB | 256 MB | 16MB
SRAM | 2 MB | 2 MB | 2MB | 1MB
FLASH | 16 MB (8 MB available to user) | 256 MB | 256MB | 6MB
Ethernet | 10/100 Mbps | 10/100 Mbps | 10/100 Mbps | 10/100 Mbps
SD Card | No | No | Yes (on CPU module host board) | No
Linux kernel | 2.6.22 | 2.6.22 | 2.6.39 | 2.6.22
Flash file system | JFFS2 | JFFS2 | JFFS2 | JFFS2

## Slide 9: Hardware Migration
Replace CPU module
2070 1E CPU module -> 2070 1C CPU module
From legacy 2070 controller
2070 1B/1E
CPU module
ATC eX 2070 CPU module

## Slide 10: Field I/O unit
2070-2E for Caltrans type cabinets
2070-2B connects to 2070-8 NEMA base
2070-2N for NEMA TS2 type 1 cabinets

## Slide 11: Serial Comms Modules
Async serial port and GPS modules (2070-7(x))
Modem modules (2070-6(x))
Fiber optic modules (2070-F(x))
Other communication modules (2070-9(x))
Notes: There are 6A, B, AE, BE, D, W
There are 7A, B
There are FX
There are 9A, B, D, E

## Slide 12: Power Supplies
Standard version (2070-4A)
NEMA version (2070-4NA)

## Slide 13: Front Panels
Emulates VT-100 terminal
8 x 40 display (2070-3B)
No display or keypad (2070-3C)

## Slide 14: 2070ATC
Chassis
2070-ATC cpu board
2070-2E+ field I/O module
2070-3B front panel
2070-4A power supply module
Comms modules as specified

## Slide 15: Software
Linus operating system
API’s
Application software packages
NTCIP (software interoperability)

## Slide 16: Standards and Specifications
ITS Cabinet Standard
ATC Controller Standard
API
Caltrans ATC 1C Standard

## Slide 17: Testing
Testing to standards is more difficult than testing to specifications
No industry-wide testing program is available
Caltrans maintains a Qualified Products List
Agency specific requirements

## Slide 18: Advantages
Open architecture eases maintenance and ensures future compatibility
Multiple application software vendors
Simple, competitive hardware purchasing
Compatible with all cabinets, existing and future
Upgradeable (hardware or software)
Fairly mature specification

## Slide 19: Disadvantages
Agencies usually must purchase software by separate agreement
Careful specifications are a must to assure proper configuration of modular components

## Slide 20: Questions?
info@mccain-inc.com